Computer Science 4630

Spring 2001

Quiz 3

True/false.  Write a clearly legible T to the left of each of the following that is true, and a clearly legible F to the left of each that is false.

- In a paged memory, the page table is used to convert from physical addresses to logical addresses.

- In a virtual memory system, moving a program to a new physical address in memory usually requires changing the addresses in the jump instructions in the program.

- Direct memory access (DMA) by devices is an important concern in the design of a virtual memory manager.

- Allowing processes to share memory is fairly simple using paged memory.

Multiple choice.  Circle the letter of the best answer.

- A serious problem with contiguous memory management is

  - relocation

  - fragmentation

  - address translation

  - implementing system calls

- If the page size in a paged system were not a power of 2, the memory management unit would have to perform what expensive operation?

  - integer division

  - integer multiplication

  - integer addition

  - factoring an integer

- In a virtual memory system, a page fault occurs when

  - a program uses a page that is outside its logical address space.

  - a program uses an array that spans several pages.

  - a program uses a page that is currently stored in physical memory.

  - a program uses a page that is currently stored on external storage, such as a disk.

- An operating system uses a two level page table to

  - speed up page table lookups.

  - avoid some page table lookups altogether.

  - make the page table occupy less memory.

  - simplify the page table lookup algorithm.

- In a virtual memory system, there is

  - one page table for the entire operating system.

  - one page table per process.

  - one page table per thread.

  - possibly several page tables for each thread.

- Segmentation

  - provides better security by allowing the logical memory to be cut into segments that reflect the logical segments of a process.

  - is just another name for virtual memory.

  - is not compatible with virtual memory.

  - is almost never used on modern computers.

- A page replacement algorithm that can be implemented without special hardware support is

  - the optimal algorithm.

  - the least-recently-used (LRU) algorithm.

  - the second chance algorithm.

  - the first-in-first-out algorithm.

- Thrashing occurs when

  - a computer  is running only compute bound processes.

  - a computer runs out of room in its process table.

  - a computer is performing a high number of page faults per second.

  - a computer is writing a large file to the disk, which prevents compute-bound processes from running.

- A response to thrashing that an operating system can make and that sometimes stops the thrashing is

  - increasing the size of the page table.

  - reducing the number of processes in memory by swapping some processes out.

  - swapping in some compute-bound processes to reduce the frequency of disk accesses.

  - increasing the amount of disk space dedicated to virtual memory.