Computer Science 4630

Spring 2001

Quiz 5

True/False.  Write a clearly legible T to the left of each of the following that is true, and a clearly legible F to the left of each that is false.

- One impediment to process migration is the presence of computers with different kinds of processors.

- Ethernet is a popular kind of wide-area network.

- In a typical cable-based Ethernet, more than one conversation among computers can be going on at once.

- A computer can only open a socket connection to a different computer, never to itself.

- For a server to support a service (such as http or ftp) the server must be running a process that waits for a connection to be requested.

Multiple choice.  Circle the letter of the best answer to each question.

- The ftp utility is used to transfer files among different computers.  It is characteristic of

  - a stand-alone (non-networked) operating system.

  - a network operating system.

  - a distributed operating system.

- A program that copies itself over network connections, moving from one computer to another, is usually called

  - a worm

  - a virus

  - a Trojan horse

  - a trap door

- The access matrix approach to protection has the advantage of

  - low space requirements

  - low time requirements

  - ease of update and upkeep

  - flexibility in expressing permissions

- Each packet sent using TCP/IP contains an address consisting of

  - An IP address and a port number.

  - An IP address and a process number.

  - A symbolic address and a port number.

  - A symbolic address and a process number.

- A file server provides stateless service if

  - The server keeps track of information about open files on client machines

  - The server does not keep track of information about open files on client machines.

  - The files that it provides are not stored physically on that server.

  - The files that it provides are stored physically on that server.

- When a server accepts a connection on a socket, it

  - continues to communicate with the client over the same socket.

  - gets a new socket from the accept operation, and communicates with the client over that socket.

  - needs to create a new socket on its own, and open a connection to the client explicitly over the new socket.

- Communication over BSD sockets is handled using

  - file system operations (read, write).

  - message passing.

  - remote procedure calls.

  - rendezvous.

- The IP protocol is primarily concerned with

  - Reliable delivery of packets between directly connected machines.

  - Reliable delivery of large (multi-packet) messages between machines that are not necessarily directly connected.

  - Routing packets through the network.

  - Maintaining long-term connections among computers.